## Slide 1: Near-Stream Computing: General and Transparent Near-Cache Acceleration
Zhengrong Wang, Jian Weng, Sihao Liu, Tony Nowatzki
UCLA
April. 2022

## Slide 2: Near-Data Computing to Decentralize Computation
Requesting Core
Remote L3 Cache
while (i < N)
C[i] = A[i] + B[i]
i++
Data movement become increasingly the bottleneck.
Computation centralized in the core.
More expensive to fetch data as system scales up.
Prefetching/streaming can only partially help.

## Slide 3: Near-Data Computing to Decentralize Computation
Requesting Core
Remote L3 Cache
while (i < N)
C[i] = A[i] + B[i]
i++
Data movement become increasingly the bottleneck.
Computation centralized in the core.
More expensive to fetch data as system scales up.
Prefetching/streaming can only partially help.
Near-data computing decentralizes the computation.
Location: memory, storage, LLC (Our Focus), …
Technology: in-situ, inorder cores, FPGA, …
Existing NDC works fall short to fully cover:
Transparency.
Synchronization-Efficiency.
Generality.
… due to inappropriate abstraction choice:
Instructions, user-defined functions, threads, …
T
E
G

## Slide 4: Features of An Ideal NDC Abstraction
Transparency.
No manual programming, auto-transformation, sequential semantics.
Synchronization-Efficiency.
Low traffic (hops) to synchronize core and offloaded NDC, alias detection.
Generality.
Arbitrary combination of memory access pattern and compute operation.
T
E
G

## Slide 5: Existing NDC Abstractions
Thread-Level NDC: Offload the entire thread context.
Examples: TOM [ISCA ’16], AMS [MICRO ’18], …
 Transparency.
 Synchronization-Efficiency.
 Generality: Works best with single data structure.
Inst-Level NDC: Offload short instruction sequences.
Examples: PIM-Enabled Inst [ISCA ’15], Omni-Compute [ISCA ’19], …
 Transparency.
 Synchronization-Efficiency: At least one request per operation.
 Generality.
User-Defined Function NDC: Offload user-defined operation.
Examples: Active Routing [HPCA ’19], Livia [ASPLOS ’20], …
 Transparency: Requires manually programming.
 Synchronization-Efficiency.
 Generality: Depends on the implementation.
T
E
G
T
E
G
T
E
G

## Slide 6: Streams: New Abstraction with Near-Data Comp.
while (i < N)
C[i] = A[i] + B[i]
i++
Stream: A decoupled seq. of addr/value.
Prevalent in data parallel workloads.
Capture long-term patterns for each data structure Rich information for transparent and general offloading.
Near-Stream Computing:
Computation scheduled along with streams.
C[i]
A[i]
B[i]

## Slide 7: Streams: New Abstraction with Near-Data Comp.
while (i < N)
C[i] = A[i] + B[i]
i++
Stream: A decoupled seq. of addr/value.
Prevalent in data parallel workloads.
Capture long-term patterns for each data structure Rich information for transparent and general offloading.
Near-Stream Computing:
Computation scheduled along with streams.
C[i]
A[i]
B[i]
+

## Slide 8: Streams: New Abstraction with Near-Data Comp.
while (i < N)
C[i] = A[i] + B[i]
i++
Stream: A decoupled seq. of addr/value.
Prevalent in data parallel workloads.
Capture long-term patterns for each data structure Rich information for transparent and general offloading.
Near-Stream Computing:
Computation scheduled along with streams.
 Transparency: Extensive compiler/ISA support.
 Efficiency: Coarser-grained range-based sync.
 Generality: Support combinations of access patterns and ops.
LLVM Compiler + GEM5 Simulator:
2.13 speedup over SOTA NDC techniques.
76% NoC traffic reduction.
C[i]
A[i]
B[i]
+

## Slide 9: Outline
Problems and Insights
NDC Taxonomy and Opportunities
Near-Stream Computing Implementation
Evaluation

## Slide 10: Taxonomy of General Near-Data Computation
Generality.
Address pattern + compute type.
// Vector Add.
while (i < N)
C[i] = A[i] + B[i]
i++
// Sum Array.
while (i < N)
S += A[i]
i++
// Indirect RMW.
while (i < N)
B[A[i]]++
i++
// Link-List Op.
while (A)
f(A->value)
A = A->next
Affine
Reduce
Multi-Op
Store
Indirect
RMW
Ptr-Chase
Load

## Slide 11: Taxonomy of General Near-Data Computation
Generality.
Address pattern + compute type.
Support all combinations.
Address Pattern Streams; Compute Type Near-Stream Operation.
Stream
Near-Stream Op

## Slide 12: Conventional vs. Near-Stream Computing

## Slide 13: Breakdown of Near-Stream Computation
54% of dynamic micro-ops can be classified as near-stream computation.
Major NS Comp.
Multi-Op Store
Ind. Ld.
Ind. RMW
Ind. Reduce
Challenging to NDC:
Inst/User-Func.
Inst/Thread
Inst/Thread
Inst/Thread
Ptr-Chase Reduce
Inst/Thread
Inst-level NDC:
always incurs high sync overheads.
Aff. Ld.
Inst

## Slide 14: Outline
Problems and Insights
NDC Taxonomy and Opportunities
Near-Stream Computing Implementation: How to …
  Embed near-stream computing in the ISA?
  Preserve sequential semantics?
  Reduce coordination overheads?
  Reuse hardware for computation?
  When to offload computation?
  …
Evaluation

## Slide 15: Near-Stream Computing ISA Overview
Explicitly encode streams and compute dependencies in the ISA.
Compiler: Recognize streams and associated computation; Transform the program.
No manually programming required.
Original Pseudo Code
N-S Computing Pseudo Code
Stream Dep. Graph
while (i < N)
v += A[i];
i++;
(a) Vector Sum
s_cfg(sa=A[i], sv+=sa);
while (i < N)
s_step(i);
v = s_load(sv);
s_end(sv, sa);
Config.
Semantically 1 load and 1 add.
Get final value.
The computation is outlined into a separate function, with the function pointer in the stream’s configuration.

## Slide 16: How to Compute with Low Overheads?
Insight: There is already a core in the remote tile.
Stream Compute Context (SCC):
Light weighted thread context.
No LSQ entries + Limited ROB entries.
Looping over configured NSC functions.
Released when streams are terminated.
Reuse existing hardware units, e.g., decoder, vector units, …
SCC

## Slide 17: Architectural Extensions
SEcore:
Mange stream configuration and offload streams.
Issue flow control credits and check for aliasing.
SEL3:
Fetch and forward operands to the consuming stream.
Coordinated by SEcore for flow control and aliasing check.
Stream Computing Manager (SCM):
Configure and terminate the stream computing context (SCC) with the near-stream function.
Simple scalar ops handled by the ALU in SEcore and SEL3 Avoid frequently accessing SCC.
SCC

## Slide 18: Range-Sync: Coarse-Grained Sync. w. Seq. Semantics
Challenges: Efficiently synchronize the core and offloaded streams.
  Flow control scheme to avoid streams running too far ahead/behind.
  Detect possible core-stream and inter-stream aliasing.
  Provide sequential semantics for transparency and context switching.
Core
SA
SB
SC
Offloaded Streams

## Slide 19: Range-Sync: Coarse-Grained Sync. w. Seq. Semantics
Challenges: Efficiently synchronize between core and streams.
Key Insight: Sync. can be coarse-grained and conservative.
  Streams tend to access individual data structures, with non-overlapping addresses.
  Aliased streams should not be offloaded at all to avoid frequent synchronization.
  Allows false positives to dramatically reduce control overheads.
Range-Sync: Only sync. every few iterations against range of touched addresses.
Core
SA
SB
SC
Offloaded Streams

## Slide 20: Timeline of Range-Sync: Normal Case
Core
Core SE
L3 SE
Allocate credits [0,R).
Translate & access element [0, R).
Collect ranges.
Check alias in ranges. Commit iteration [0,R).
Send commits [0,R).
Allocate more credits.
Writeback & release states [0, R).
Pipelined to
hide latency.
Credits [0, R)
Ranges [0, R)
Ranges [0, R)
Committed [0, R)
Commits [0, R)
Done [0, R)
Key Takeaway:
Sync every R iterations.
Check alias against ranges.
Overheads: 4/R NoC msg. per affine element.

## Slide 21: Timeline of Range-Sync: Alias/Context Switch in Core
Core
Core SE
L3 SE
Allocate credits [0,R).
Translate & access element [0, R).
Collect ranges.
Alias/context switch at iteration M (M < R).
Send commits [0,M).
Continue stream in core.
Writeback & release states [0, M). End.
Pipelined to
hide latency.
Credits [0, R)
Ranges [0, R)
Ranges [0, R)
Committed [0, M)
Commits [0, M) & End
Done [0, M)
Key Takeaway:
Execution continues at iteration M with streams in core.
Still provide precise states.

## Slide 22: Sync-Free Optimized NSC
Access & writeback element [0, R).
Access & writeback element [0, R).
Core
Core SE
L3 SE
Allocate credits [0,R).
Access & writeback element [0, R).
Allocate more credits.
Pipelined to
hide latency.
Credits [0, R)
Done [0, R)
Key Takeaway:
Pragma disables synchronization.
Offloaded streams can directly commit.
Coarse-grained context switch at iteration n*R.
Fully decoupled loops can be removed.
Simultaneously execute multiple loops.
More details in the paper:
Compiler transformation.
Nested stream configuration.
Avoid deadlocks.
Determine when to offload.
…

## Slide 23: Outline
Problems and Insights
NDC Taxonomy and Opportunities
Near-Stream Computing Implementation
Evaluation

## Slide 24: Configurations
LLVM-based compiler to recognize streams and transform programs.
Gem5 20.0 cycle-level execution-driven simulator.
14 data processing workloads from Rodinia and Gap Graph Suite.
  Parallelized with OpenMP, with AVX-512 enabled.
Configurations (see paper for details):
  8x8 mesh topology, 3-level MESI, 32kB L1 I/D, 256kB L2, 1MB L3.
  Base: Baseline cores with L1/L2 prefetchers. No stream support.
  Inst-Level NDC (INST): Computation is offloaded at instruction level to LLC.
  User-Def Func. NDC (UDF): Single operand UDF is offloaded at loop level.
  NScore: Use SEcore as a prefetcher at the core [ISCA ’19].
  NSno comp: Streams are offloaded to LLC, but no computation [HPCA ’21].
  NS: Near-stream computations offloaded to LLC, with range-sync [this work].
  NSno sync/NSdecouple: Disable range-sync and fully decouple loops [this work].
Resembles SOTA NDC:
Omni-Compute [ISCA ’19]
Livia [ASPLOS ’20]

## Slide 25: Overall Speedup with OOO8
Chart: 
| pathfinder | srad | hotspot | hotspot3D | histogram | scluster | svm | bfs_push | pr_push | sssp | bfs_pull | pr_pull | bin_tree | hash_join | geomean.
NScore | 1.0551 | 0.89602 | 0.99841 | 1.0377 | 0.91844 | 1.7707 | 4.2919 | 1.2488 | 4.3458 | 1.1002 | 1.3713 | 1.3786 | 1.3844 | 1.1582 | 1.4108
NSno comp | 1.7295 | 0.98443 | 1.4983 | 1.0845 | 0.92224 | 1.8826 | 5.1557 | 1.8288 | 4.3282 | 1.4866 | 1.9025 | 1.8925 | 2.8647 | 2.4102 | 1.8867
INST | 1.9145 | 0.95448 | 1.4298 | 2.2941 | 1.0554 | 1.6189 | 4.286 | 1.2556 | 10.3628 | 1.1856 | 1.2736 | 1.4227 | 1.3853 | 1.1585 | 1.7191
UDF | 1.0667 | 0.85526 | 0.96543 | 1.0138 | 1.0554 | 1.6189 | 4.286 | 1.2556 | 10.3628 | 1.1856 | 1.2858 | 1.4528 | 10.0854 | 9.2787 | 2.0105
NS | 4.1867 | 3.009 | 2.8939 | 5.2056 | 1.1359 | 2.4582 | 8.0155 | 1.5612 | 27.7055 | 1.6129 | 2.1581 | 2.6308 | 2.8683 | 2.408 | 3.1964
NSno sync | 4.6046 | 3.0772 | 3.4669 | 5.9266 | 1.1363 | 2.4494 | 8.1215 | 2.2779 | 36.1421 | 1.8883 | 2.1551 | 2.5972 | 2.8683 | 2.408 | 3.4886
NSdecouple | 0 | 0 | 0 | 0 | 0 | 0.015677 | 0.080735 | 0.26266 | 1.9483 | 0.06586 | 0.16567 | 0 | 7.2171 | 6.8707 | 0.77761
27.7
38.1
36.1
NS achieves 1.85x speedup over INST. (2.12x for NSdecouple over UDF).
Range-sync incurs low overheads as NS is only 8% slower than NSno sync.

## Slide 26: Dynamic Micro Ops Breakdown
Generality: NSC captures 54% of dynamic micro-ops.
93% of possible ops are offloaded.

## Slide 27: NoC Traffic Breakdown
INST and UDF reduces NoC traffic by 50% and 40% respectively.
NS reduces NoC traffic by 69% (76% by NSdecouple).
NS offloads at stream granularity and incurs low overheads using range-sync.
Control
Data
NDC
Chart: Travelled Hops
| pathfinder | srad | hotspot | hotspot3D | histogram | scluster | svm | bfs_push | bfs_push_check | pr_push | sssp | sssp_check | bfs_pull | pr_pull | bin_tree | hash_join | avg.
Base | 0.38288 | 0.37408 | 0.39328 | 0.4024 | 0.41876 | 0.37204 | 0.41557 | 0.47084 | 0.35849 | 0.54032 | 0.50927 | 0.36991 | 0.30839 | 0.3092 | 0.25498 | 0.2542 | 0.38341
BG Data | 0.61712 | 0.62592 | 0.60672 | 0.5976 | 0.58124 | 0.62796 | 0.58443 | 0.52916 | 0.64151 | 0.45968 | 0.49073 | 0.63009 | 0.69161 | 0.6908 | 0.74502 | 0.7458 | 0.61659
BG Strm | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
INST | 0.0031564 | 0.17232 | 0.00058672 | 0.0004327 | 0.41153 | 0.28493 | 0.21117 | 0.02538 | 0.24027 | 0.012296 | 0.038306 | 0.24893 | 0.23037 | 0.16347 | 0.10177 | 0.093095 | 0.13988
OMNI Data | 0.0055469 | 0.2527 | 0.00085594 | 0.00063555 | 0.57246 | 0.41426 | 0.31756 | 0.044864 | 0.40771 | 0.019046 | 0.06176 | 0.39412 | 0.45646 | 0.36856 | 0.28538 | 0.26389 | 0.24161
OMNI Strm | 0.21156 | 0.24568 | 0.35849 | 0.27267 | 0.007216 | 0 | 0 | 0.15273 | 0.0013554 | 0.11054 | 0.094634 | 0 | 0.012086 | 0.0072484 | 0 | 0 | 0.092138
UDF | 0.34367 | 0.36729 | 0.39092 | 0.40473 | 0.41153 | 0.28493 | 0.21117 | 0.02538 | 0.24027 | 0.012296 | 0.038306 | 0.24893 | 0.23672 | 0.16619 | 0.010481 | 0.010837 | 0.21273
LIVIA Data | 0.56677 | 0.61759 | 0.60231 | 0.59419 | 0.57246 | 0.41426 | 0.31756 | 0.044864 | 0.40771 | 0.019046 | 0.06176 | 0.39412 | 0.46262 | 0.37274 | 0.047241 | 0.025359 | 0.34504
LIVIA Strm | 0 | 0 | 0 | 0 | 0.007216 | 0 | 0 | 0.15273 | 0.0013554 | 0.11054 | 0.094634 | 0 | 0 | 0 | 0.19671 | 0.25374 | 0.051058
NS | 0.0032515 | 0.00059059 | 0.0005794 | 0.00043479 | 0.0028013 | 0.098781 | 0.067127 | 0.085617 | 0.20744 | 0.057602 | 0.065311 | 0.18962 | 0.2331 | 0.1751 | 0.010515 | 0.010809 | 0.075542
SC-Sync Data | 0.0093738 | 0.058279 | 0.092855 | 0.056696 | 0.1575 | 0.14292 | 0.10869 | 0.11368 | 0.26729 | 0.0063488 | 0.10046 | 0.27593 | 0.22883 | 0.14257 | 0.21989 | 0.093611 | 0.12968
SC-Sync Strm | 0.048442 | 0.058512 | 0.059836 | 0.048417 | 0.030573 | 0.0013033 | 0.0092383 | 0.18294 | 0.016498 | 0.065867 | 0.11311 | 0.01405 | 0.019818 | 0.016574 | 0.21335 | 0.26741 | 0.072872

## Slide 28: Energy vs. Speedup
NS and NSdecouple achieves 2.85/3.52 energy efficiency over OOO8.
Both small inorder cores and large OOO cores benefit from NSC.

## Slide 29: Conclusion
Near-Stream Computing:
 Transparency: Extensive compiler/ISA support.
 Efficiency: Coarser-grained range-based sync.
 Generality: All combinations of address pattern + compute type.
Core Idea: Encode access patterns and compute deps in ISA.
Expose rich semantic information to the hardware.
Programmer-friendly near-data architectures.
T
E
G